## Slide 1
Wind and Solar Energy Resources
Modeling and Analysis
Technical Presentation
By
Mohamed Abuella
The University of North Carolina at Charlotte
August 6th, 2019

## Slide 2
Solar Energy Resources
Modeling
Wind Energy Resources
Modeling
Presentation Outline

## Slide 3
Four U.S. Locations for Comparison of Renewable Energy Modeling and Analysis
Charlotte NC, Boston MA, Boulder CO, Tucson AZ.
For Different Locations in the U.S.
Data are retrieved from NREL’s Developer Network: https://developer.nrel.gov/
Wind and Solar Energy Resources Modeling and Analysis

## Slide 4
Charlotte, NC
Boston, MA
Boulder, CO
Tucson, AZ
Time series of wind speed at height 100m (m/s)
Wind Energy Resources Modeling

## Slide 5
Charlotte, NC
Boston, MA
Boulder, CO
Tucson, AZ
Boxplots of monthly distribution of wind speed
Wind Energy Resources Modeling

## Slide 6
Charlotte, NC
Boston, MA
Boulder, CO
Tucson, AZ
Wind Roses of Wind Speed
Distribution of wind direction and speed
Wind Energy Resources Modeling

## Slide 7
Charlotte, NC
Boston, MA
Boulder, CO
Tucson, AZ
Probability density distribution of wind speed
Wind Energy Resources Modeling

## Slide 8
Charlotte, NC
Boston, MA
Boulder, CO
Tucson, AZ
Wind turbine GE 1.5SLE 77m is utilized for modeling
The wind power curve for GE 1.5SLE 77m
to covert the wind speed to wind power
http://www.wind-power-program.com/Downloads/Databasepowercurves(May2017).zip
Wind Energy Resources Modeling

## Slide 9
Charlotte, NC
Boston, MA
Boulder, CO
Tucson, AZ
Probability density distribution of wind power
Considering other parameters such as air pressure, temperature and density at the given height=100m
Wind Energy Resources Modeling

## Slide 10
Charlotte, NC
Boston, MA
Boulder, CO
Tucson, AZ
Month0 | MWh | NCF
1 | 467.945 | 41.90%
2 | 584.361 | 58.00%
3 | 510.499 | 45.70%
4 | 512.191 | 47.40%
5 | 420.662 | 37.70%
6 | 239.808 | 22.20%
7 | 354.663 | 31.80%
8 | 285.923 | 25.60%
9 | 396.328 | 36.70%
10 | 504.488 | 45.20%
11 | 471.683 | 43.70%
12 | 691.553 | 62.00%
Month | MWh | NCF
1 | 387.574 | 34.70%
2 | 455.725 | 45.20%
3 | 410.236 | 36.80%
4 | 456.256 | 42.20%
5 | 381.352 | 34.20%
6 | 193.475 | 17.90%
7 | 230.690 | 20.70%
8 | 141.379 | 12.70%
9 | 197.738 | 18.30%
10 | 310.630 | 27.80%
11 | 355.663 | 32.90%
12 | 298.279 | 26.70%
Month | MWh | NCF
1 | 413.396 | 37.00%
2 | 288.217 | 28.60%
3 | 382.094 | 34.20%
4 | 339.568 | 31.40%
5 | 222.077 | 19.90%
6 | 187.928 | 17.40%
7 | 216.100 | 19.40%
8 | 215.737 | 19.30%
9 | 268.648 | 24.90%
10 | 206.966 | 18.50%
11 | 224.898 | 20.80%
12 | 312.770 | 28.00%
Month0 | MWh | NCF
1 | 262.764 | 23.50%
2 | 247.664 | 24.60%
3 | 259.804 | 23.30%
4 | 378.228 | 35.00%
5 | 184.679 | 16.50%
6 | 188.630 | 17.50%
7 | 111.523 | 10.00%
8 | 143.448 | 12.90%
9 | 223.078 | 20.70%
10 | 258.261 | 23.10%
11 | 236.885 | 21.90%
12 | 274.958 | 24.60%
Wind Energy Modeling
in 2009
Calculating the net capacity factor (NCF)
for each month, then over the entire year
NCF=
NCF=
Wind Energy Resources Modeling

## Slide 11
Wind Energy Modeling
in 2009 and 2010
2009 | MWh | NCF
Charlotte | 3818.9 | 29.1%
Boulder | 3278.4 | 24.9%
Boston | 5440.1 | 41.4%
Tucson | 2769.9 | 21.1%
2010 | MWh | NCF
Charlotte | 3544.6 | 27.0%
Boulder | 2676.9 | 20.4%
Boston | 6107.7 | 46.5%
Tucson | 2969.9 | 22.6%
Chart: Yearly Net Capacity Factor
| Charlotte | Boulder | Boston | Tucson
2009 | 0.23144 | 0.25507 | 0.23448 | 0.24269
2010 | 0.27 | 0.204 | 0.465 | 0.226
Chart: Yearly Yeild of Wind Energy
| Charlotte | Boulder | Boston | Tucson
2009 | 3819 | 3278 | 5440 | 2770
2010 | 3545 | 2677 | 6108 | 2970
Wind Energy Resources Modeling

## Slide 12
Time series of components of solar irradiance, GHI, DNI, DHI (W/m2)
Solar Energy Resources Modeling

## Slide 13
Global Horizontal Irradiance (GHI) at the plane of array (POA)
Solar Energy Resources Modeling

## Slide 14
Pvlib Toolbox from Sandia and NREL’s SAM package and Weather Data from GFS Global Model
https://pvlib-python.readthedocs.io/en/latest/introexamples.html
https://pvlib-python.readthedocs.io/en/latest/forecasts.htm
To convert the solar irradiance to solar PV power, besides the cloud cover and radiative transfer model, other parameters are considered, such as air temperature at the plane of array, module orientation and efficiency .
Convert GHI at the POA to Solar PV Power
PV Module CS5P-220M
Manufacturer: Canadian Solar Type: Polycrystalline Cells
Power: 220 W (Maximum)
Length: 63.1in (1,602mm)
Width: 41.8in (1,061mm)
Depth: 1.6in (40mm)
https://www.solarover.com/panels/cs5p.pdf
Solar Energy Resources Modeling

## Slide 15
Time series of Solar Power (W), for a solar plant with 15*300 PV modules (220W for each)
Solar Energy Resources Modeling

## Slide 16
2009 | Wh | NCF |  | 2010 | Wh | NCF
Charlotte | 446028 | 23.14% |  | Charlotte | 446035 | 23.14%
Boulder | 491571 | 25.51% |  | Boulder | 491582 | 25.51%
Boston | 451885 | 23.45% |  | Boston | 451899 | 23.45%
Tucson | 467719 | 24.27% |  | Tucson | 467726 | 24.27%
Chart: Yearly Yield of Solar Energy
| Charlotte | Boulder | Boston | Tucson
2009 | 446.0278 | 491.5714 | 451.8849 | 467.7191
2010 | 446.0346 | 491.5816 | 451.8991 | 467.7258
Chart: Yearly Net Capacity Factor
| Charlotte | Boulder | Boston | Tucson
2009 | 0.23144 | 0.25507 | 0.23448 | 0.24269
2010 | 0.23144 | 0.25508 | 0.23448 | 0.2427
Solar Energy Resources Modeling
For 1 PV module (220W, PV Module CS5P-220M)
Calculating the total energy and net capacity factor, as it is done in the wind energy modeling
Here, to exclude the variability from the PV output, the clear-sky irradiance is used for conversion to the PV AC Power over the entire year. This leads to capture similar PV output for other years as well.

## Slide 17
2009 | NCF | 
 | Wind Energy | Solar Energy
Charlotte | 29.10% | 23.14%
Boulder | 24.90% | 25.51%
Boston | 41.40% | 23.45%
Tucson | 21.10% | 24.27%
Chart: 2009 Net Capacity Factor
| Charlotte | Boulder | Boston | Tucson
Wind Energy | 0.291 | 0.249 | 0.414 | 0.211
Solar Energy | 0.23144 | 0.25507 | 0.23448 | 0.24269
Chart: 2010 Net Capacity Factor
| Charlotte | Boulder | Boston | Tucson
Wind Energy | 0.27 | 0.204 | 0.465 | 0.226
Solar Energy | 0.23144 | 0.25507 | 0.23448 | 0.24269
2010 | NCF | 
 | Wind Energy | Solar Energy
Charlotte | 27.00% | 23.14%
Boulder | 20.40% | 25.51%
Boston | 46.50% | 23.45%
Tucson | 22.60% | 24.27%
Comparison of NCF for Resources of Wind & Solar Energy
Wind and Solar Energy Resources Modeling

## Slide 18
Wind and Solar Energy Resources Modeling
Conclusion
The performance of wind and solar energy resources depends significantly on their location and weather conditions.
Further Work
Modeling and evaluate the wind and solar resources backed up by energy storage systems.
References
https://www.r-bloggers.com/time-series-analysis-with-wind-resource- assessment-in-r/
https://github.com/mhdella/AWEA_WRA_Working_Group/blob/master/Example_Wind_Resource_Assessment_Using_R.md
https://pvlib-python.readthedocs.io/en/latest/introexamples.html
Stein, J. S., Holmgren, W. F., Forbess, J., & Hansen, C. W. (2016, June). PVLIB: Open source photovoltaic performance modeling functions for Matlab and Python. In 2016 ieee 43rd photovoltaic specialists conference (pvsc) (pp. 3425-3430). IEEE.
Blair, N., Dobos, A. P., Freeman, J., Neises, T., Wagner, M., Ferguson, T., ... & Janzou, S. (2014). System advisor model, sam 2014.1. 14: General description (No. NREL/TP-6A20-61019). National Renewable Energy Lab.(NREL), Golden, CO (United States).

## Slide 19
Thanks for Listening
Any Question?
http://epic.uncc.edu/
Mohamed Abuella
https://mohamedabuella.github.io
Energy Production and Infrastructure Center
University of North Carolina at Charlotte