## Slide 1
Hourly Probabilistic Solar Power Forecasts
Energy Production and Infrastructure Center
Department of Electrical and Computer Engineering
University of North Carolina at Charlotte
Mohamed Abuella
Prof. Badrul Chowdhury
September 18, 2017

## Slide 2
Hourly Probabilistic Forecasting of Solar Power
Overview of Solar Power Forecasting
Presentation Outline

## Slide 3
Mohamed Abuella
An electrical engineer by training, traditionally is interested in Mathematical and Computational Analysis, Modeling and Optimization, and who is recently get passionate in Artificial Intelligence and Data-driven Analytics for Energy and Smart Grid applications.
Hobbies and Interests
Making Mediterranean Food and Drink, but also try my own wired recipes;
Stretching, Walking, Running, or Swimming, ..and hopefully Climbing; Wondering around and Discovering New Places, ..kind of adventure;
Watching, Reading and Sharing Stuff on Internet, useful & dumb things;
And more often just.. Chilling and Enjoy Doing Nothing!

## Slide 4
Renewables Generations
(Wind and Solar) are Too Variable
High Efficiency and Large Energy Storage
Still not Exist
Reducing
Cost
and Pollution
Why Forecast?
PG = PD + Ploss
Variable Generations (V.G.) Forecasting

## Slide 5
VG forecasting in US. electric utilities and ISO, such as CAISO, ERCOT, MISO, ISO-NE, NYISO,…etc.
Botterud, J. Wang, V. Miranda, and R. J. Bessa, “Wind power forecasting in US electricity markets,” The Electricity Journal, vol. 23, no. 3, pp. 71–82, 2010.
Elke Lorenz, “Solar Resource Forecasting” International Solar Energy Society (ISES) Webinar, 2016.
Voyant, C., Notton, G., Kalogirou, S., Nivet, M. L., Paoli, C., Motte, F., & Fouilloy, A. (2017). Machine learning methods for solar radiation forecasting: A review. Renewable Energy, 105, 569-582.
Forecast Horizons
Variable Generations (V.G.) Forecasting
Forecast horizons, forecasting models and the related applications of VG forecasts
Where Forecast?

## Slide 6
Flowchart of the Combined Approach (Physical and Statistical) of the Solar Power Forecasting
Regression
Extrapolation
Solar Power Forecasting
How Forecast?

## Slide 7: Flowchart of the Solar Power Forecasting
Hourly Probabilistic Forecasting of Solar Power

## Slide 8
Data Description:
https://crowdanalytix.com/contests/global-energy-forecasting-competition-2014-probabilistic-solar-power-forecasting
http://www.ecmwf.int (European Centre for Medium-Range Weather Forecasts)
Hourly Probabilistic Forecasting of Solar Power
Weather predictions are produced by a global numerical weather prediction system, European Centre for Medium-Range Weather Forecasts (ECMWF).
Data partition into training and testing sets
No. | Input Variable, (X)
10 | Surface thermal radiation down
11 | Top net solar radiation
12 | Total precipitation
13 | Heat Index
14 | Wind Speed
15 | Hours
16 | Months
17 | Days of Month
18 | Days of Year
Timeline | Month | Year | Partition
From | April | 2012 | Training Set
To | May | 2013 | 
From | June | 2013 | Testing Set
To | May | 2014 | 
No. | Input Variable, (X)
1 | Cloud Water Content
2 | Cloud Ice Content
3 | Surface Pressure
4 | Relative Humidity
5 | Cloud Cover
6 | 10m - U Wind
7 | 10m - V Wind
8 | 2-m Temperature
9 | Surface solar radiation down
PV solar system is near Canberra, Australia, consisting of 8 panels, its nominal power of (1560W), and panel orientation 38° clockwise from the north, with panel tilt (of 36°). The historical observed solar power data are normalized to the rated capacity (i.e., 1560W).

## Slide 9
Multiple Linear Regression (MLR) Analysis, Artificial Neural Networks (ANN), and Support Vector Regression (SVR) are deployed for the short-term solar power forecasting.
Flowchart of the forecasting models
Training Set
Solar Power Forecast
Learning Algorithm
New Input X
Predicted Output Y
Flowchart of solar forecasting model building steps
Building the Model
Training
Validation
Testing
Forecasting Models
Parametric and Nonparametric Models
T. Hastie, R. Tibshirani, J. Friedman, and others, The elements of statistical learning, 2nd Edition. Springer-Verlag New York, 2009.

## Slide 10
General diagram of combining different models
Combining Various Models
Methods of Combining The Models
Random forest (RF) is chosen to be the ensemble learning method for combining the various models’ outcomes.
Fcomb=WA*MA+ WB*MB + WC*MC ….+ WN*MN
WN is a weight is assigned to the outcome of a model MN
Ensemble Forecasts
T. Hastie, R. Tibshirani, J. Friedman, and others, The elements of statistical learning, 2nd Edition. Springer-Verlag New York, 2009.
Model N
Weather Data
Ensemble Learning (RF) for Combining of Forecasts
Combined Forecasts
Individual Forecasts of PV Solar Power
Model A
Model B

## Slide 11
Day | Month
1 : | June
: | July
: : : | : : :
: | April
30 | May
31 | 00:00 : 23:00
Weather Data | 
: : | : :
: | :
: : : | : : :
: | :
: | :
: : : | : : :
PV Power | 
: : | (Past Observations)
: | 
: : : | 
: | 
: | 
Forecasts (Model’s Outcomes) | 
at 00:00
Day | Month
1 : | June
: | July
: : : | : : :
: | April
30 | May
31 | 00:00 : 23:00
Weather Data | 
: : | : :
: | :
: : : | : : :
: | :
: | :
: : : | : : :
Models’ Outcomes |  | 
: : | : : | : :
: | : | :
: : : | : : : | : : :
: | : | :
: | : | :
Forecasts |  | 
PV Power | 
: : | (Past Observations)
: | 
: : : | 
: | 
: | 
Combined Forecasts | 
(a)
(b)
Persistence model and day-ahead Forecasts from MLR, ANN and SVR
Combining by Radom Forest
Producing Different Models’ Outcomes
Schematic diagram of producing and ensemble different models’ outcomes
Ensemble Forecasts

## Slide 12
Probabilistic Forecasts
Ensemble-based probabilistic forecasts method:
Probabilistic model
Solar power point forecasts
NWP point forecasts
Probabilistic forecasts of solar power
(a)
(b)
(c)
Diagram of ensemble-based probabilistic forecasts,
Splitting mechanism of trees in random forest,
Sample of ensemble-based probabilistic forecasts of solar power of 3 days

## Slide 13
Analog Ensemble (AnEn) method:
S. Alessandrini, L. Delle Monache, S. Sperati, and G. Cervone, “An analog ensemble for short-term probabilistic solar power forecast,” Appl. Energy, vol. 157, pp. 95–110, 2015.
Probabilistic Forecasts
where denotes the given point forecast at an hour Hr, for which the prediction interval will be estimated, the point forecasts at the same hour of the day.
Notice that all values are normalized in the range [0, 1].
Schematic diagram of analog ensemble method
= 0.1

## Slide 14
Persistence probabilistic forecasts method:
Probabilistic Forecasts
Schematic diagram of analog ensemble method
The 10, 20 and 30 recent observed powers are carried out.
It is found that the recent 10 observed solar powers at the given hour with CDF distribution achieve more accurate persistence probabilistic forecasts.
No past forecasts are needed.

## Slide 15
Probabilistic Forecasts
Different distributions of probability
Probability distributions by the cumulative distribution function (CDF)
Linear CDF
Max
Min
to derive CDF
Parametric normal- distributed CDF
Mean
Std. dev.
to derive CDF.
Nonparametric CDF
No mean
neither Std. Dev.
CDF is estimated by piecewise nonparametric method
The probabilistic forecasts are estimated by using CDF-1
For example, for a given point forecast at 14:00, June 2nd 2013:
Histogram of the ensemble of RF’s outcomes

## Slide 16
Probabilistic Forecasts
Different distributions of probability
Probability distributions by the cumulative distribution function (CDF)
Linear CDF
Max
Min
to derive CDF
Parametric normal- distributed CDF
Mean
Std. dev.
to derive CDF.
Nonparametric CDF
No mean
neither Std. Dev.
CDF is estimated by piecewise nonparametric method
The probabilistic forecasts are estimated by using CDF-1
Histogram of the ensemble of RF’s outcomes
For example, for a given point forecast at 12:00, May 29th 2014:

## Slide 17
The objective is to determine probabilistic solar forecasts in the form of probabilistic distribution (in quantiles) in incremental time steps through the forecast horizon.
A Pinball loss function is used to evaluate the accuracy of the probabilistic forecasts. It is a piecewise linear function which is often used to evaluate the accuracy of quantile forecasts.
J. M. Morales, A. J. Conejo, H. Madsen, P. Pinson, and M. Zugno, Integrating renewables in electricity markets - Operational problems, vol. 205. Boston, MA: Springer US, 2014.
where Pbq(F, P) is the pinball loss function to the probabilistic forecasts for each hour; is the forecasted value at the certain q quantile of the probabilistic solar power forecasts, and P is the observed value of the solar power. The quantile q has discrete values .For instance, q = 0.9 means that there is a 90% probability that the observed solar power will be less than the value of the 90th quantile.
Probabilistic Forecasts
Evaluation of probabilistic forecasts:

## Slide 18
Graphs of the probabilistic forecasts of the three methods for three days
Results and Evaluation
The lower Pinball (Pb) is, the more accurate probabilistic forecasts are.
Pinball loss function (Pb):

## Slide 19
Monthly Pinball of the probabilistic forecasts of the three methods
Results and Evaluation
Pinball loss function (Pb):
The lower Pinball (Pb) is, the more accurate probabilistic forecasts are.

## Slide 20
Results and Evaluation
Chart: The Improvements of Ensemble over Analog Ensemble
| June | July | August | September | October | November | December | January | February | March | April | May
AnEn | 0.016105 | -0.017583 | -0.050525 | 0.012754 | 0.0028841 | -0.016703 | 0.0071909 | 0.038367 | 0.058032 | -0.02011 | 0.034124 | 0.067554
Chart: Probabilistic Forecasts
| June | July | August | September | October | November | December | January | February | March | April | May
Persistence | 0.01658 | 0.017596 | 0.018245 | 0.017307 | 0.014922 | 0.019083 | 0.016202 | 0.017876 | 0.02146 | 0.020811 | 0.019437 | 0.013709
Analog Ensemble | 0.0096912 | 0.012198 | 0.011126 | 0.011633 | 0.009605 | 0.010398 | 0.0089507 | 0.0083014 | 0.01039 | 0.01281 | 0.010258 | 0.0085945
Ensemble | 0.0095352 | 0.012413 | 0.011689 | 0.011484 | 0.0095773 | 0.010571 | 0.0088863 | 0.0079829 | 0.0097872 | 0.013068 | 0.0099075 | 0.0080139

## Slide 21: Conclusions
The probabilistic forecasting are quantifying the uncertainty associated with point forecasts.
Combining the forecasts of various models leads to accurate point and probabilistic forecasts.
Throughout the complete year, the ensemble based-probabilistic forecasts are more accurate. than the analog ensemble and persistence probabilistic forecasts.
The random forest is a powerful ensemble learning method.
The CDF with the assumption of a normal distribution is better than the linear distribution to produce the probabilistic forecasts.
The nonparametric estimation of CDF without the normality assumption yields a small improvement (Pb=0.0100 vs. Pb=0.0102 with a normality assumption of CDF).
With additional historical data, the forecasting performance could be improved.

## Slide 22
Thanks for Your Listening
Any Question?
http://epic.uncc.edu/
Mohamed Abuella
mabuella@uncc.edu
Energy Production and Infrastructure Center
University of North Carolina at Charlotte